C is a high level structured language developed by Dennis Ritchie(Bell Labs – around 1970) used to interact more directly with computer`s hardware & memory.

Programming is a process of designing & building an executable computer program to accomplish a specific computing task.

Algorithm is a finite set of well-defined instructions or steps used to solve a particular problem or perform a task.

The ‘#include’ statement is a preprocessor directive used to include a header file.

Flowcharts are simple visual tools that help us understand
& represent processes very easily. It is a graphical representation of algorithm.

Symbols in Flowcharts:
- Terminal/Terminator – Oval shape indicating start, stop & halt.
- I/O – Parallelogram indicating input & output.
- Action/Process – Rectangle box indicating arithmetic instructions, specific action or operation.
- Decision – Diamond shape indicating a decision point.
- On-page connector/reference – small circle indicating reference on same page.
- Off-page connector/reference – Pentagon indicating reference on different page.
- Flow line – Arrows indicating direction of flow.

Rules of Flowchart
- Opening statement must be ‘start’ keyword.
- Closing statement must be ‘end’ keyword.
- All symbols must be connected with arrow line.
- Each decision point must have 2 or more distinct outcomes.
- Flow should generally move from top to bottom or left to right.

Compiler is a special program that translates entire high level source code of program into machine(binary) code. It reads code, checks for errors, & then converts it into executable file. Its language examples are C, C++ & Java.

A compiled code can run multiple times without recompiling.

Interpreter is a type of language processor that translates & executes a program line by line. It is slower than compiler. Its language examples are Python, JavaScript, PHP & Ruby.

Structure of C program
- Documentation – a comment describing program
- Preprocessor – includes header file
- Definition - ‘#define’ for setting up a word that replaces other
- Global Declaration
- Main Function – void main() does not return any value while int main() does return a value.
- Sub Program – user defined functions other than main function

Programming style in C
- Use meaningful variable names
- Use proper indentation & spacing
- Add comments for explanation
- Use consistent naming conventions
- Break long codes into functions for clarity

C tokens are basic building blocks of any C program
- Keywords – reserved words with special meanings
- Identifier – names given to various program elements such as variables, functions, arrays etc..
- Constants – value assigned to variable. You could make a value of variable constant throughout program by adding const before variable defining.
- String Literals – sequence of characters enclosed in double quotes
- Operator – symbols specifying operations
- Special Symbols
  {} braces – block of code
  [] brackets – array of brackets
  () parentheses – function brackets
  ; semicolon – statement terminator
  # hash – preprocessor directive
  , comma
  \ back slash – escape character

Separators are symbols or characters used to group & organize code. Its examples are {}, (), [], semicolon, \n, \t(for indentation) & comma.

Variable is a named memory location to store data. It has a name(identifier), data type & value. It must be declared before use.

Rules for naming Identifiers
- It must start with letter or underscore
- It should not have space or special character
- It should not be same as keywords

Primary/Primitive/Basic Data Types
- int – whole numbers – 2 to 4 bytes – %d
- float – decimal numbers – 4 bytes – %f
- double – precision float – 8 bytes – %lf
- char – single chaarcter – 1 byte – %c

Derived Data Types – These are built from basic data types & allows more complex data handling.
- Array – It is a collection of elements of same type stored in contiguous memory locations.
- Pointer – It is a variable that stores memory address of another variable.
- Structure(struct) – It is a user defined data type that allows grouping of variables of different types.

Declaration of variable means telling the compiler the name & data type of variable.

Arithmetic Operators
- Addition +
- Substraction -
- Multiplication *
- Division /
- Modulus % - it gives remainder of division as output.

Boolean Output
If stated relationship is true, then its 1 otherwise its 0.

Relational Operators
- Equal to ==
- Not equal to !=
- Greater than >
- Less than <
- Less than or equal to <=
- Greater than or equal to >=

Logical Operators
- Logical AND && - returns 1 only if both operands are true(1)
- Logical OR || - returns 1 if either operand is true
- Not ! – reverses boolean output

Assignment Operators
- Simple assignment =
- Addition assignment +=
- Substraction assignment -=
- Multiplication assignment *=
- Division assignment /=
- Modulus assignment %=
- bw AND assignment &=
- bw OR assignment |=
- bw XOR assignment ^=
- bw right shift assignment >>=
- bw left shift assignment <<=

Increment/Decrement Operators
- PreIncrement (++x) – value changes immediately
- PostIncrement (x++) - value changes after 1 step
- PreDecrement (--x)
- PostDecrement (x--)

Bitwise Operators – manipulate bits of binary number enabling efficient low level operations.
- AND (&) – same then 1 otherwise 0
- OR (|) – if either is 1 then 1 otherwise 0
- XOR (^) – different then 1 otherwise 0
- NOT (~) – inverts all
- Left shift (<<) – shifts binary bits to left
- Right shift (>>) – shifts binary bits to right

Special Operators
sizeof – it returns the size(in byte) of variable or data type.
int x;
printf("Size of int: %zu bytes\n", sizeof(int));
printf("Size of x: %zu bytes\n", sizeof(x));

Comma Operator(,)
int a = 1, b = 2, c;
c = (a++, b++);
// a becomes 2, b becomes 3, c gets the value of b (3)

Address-of Operator(&) - It returns memory address of its operand.
int num = 10;
int *ptr;
ptr = &num;
// ptr now holds the memory address of num

Dereference Operator (*) - It accesses memory stored by address-of operator.
int num = 10;
int *ptr = &num;
printf("Value at address: %d\n", *ptr);
// Prints 10

Conditional / Ternary Operator (? :)
int age = 20;
char *status = (age >= 18) ? "Adult" : "Minor";
printf("Status: %s\n", status);
// Prints "Adult"

Member Selection Operators (. and ->)
. is used to direct access members of structures or union.
-> is used to access members through pointers.
    struct Point {int x;int y;};
    struct Point p1 = {10, 20};
    struct Point *p_ptr = &p1;

    printf("Direct access: %d\n", p1.x);
    printf("Pointer access: %d\n", p_ptr->y);

Cast Operator is used for explicit type conversion & is aka type casting. (data_type) expression;

Operator Precedence & Associativity
1. -> . a++ a-- L to R
  ++a --a +,-(unary) ! ~ R to L
2. cast, dereference, addressof, sizeof
3. * / % L to R
4. + -
5. << >>
6. < <= > >=
7. == !=
8. bw AND
9. bw XOR
10. bw OR
11. AND
12. OR
13. Ternary R to L
14. Assignment
15. Comma L to R

Mathematical Functions
- are available through “math.h”.
- sin(x), cos(x), tan(x), asin(x), acos(x), atan(x)
- sqrt(x) – square root
- pow(base, exponent)
- log(x) – natural log
- log10(x) – common log
- exp(x) – e raised to power of x
- ceil(x) – returns smallest integer >=x
- floor(x) – returns largest integer <=x
- round(x) – rounds up x
- fabs(x) – returns absolute value of float x
- abs(x) – returns absolute value of int x
- fmod(x, y) – returns float remainder of x divided by y

I/O Operations
- Formatted – printf and scanf
- Unformatted – getchar(), putchar(), gets(), puts()
  getchar() - reads single character from input
  putchar() - writes single character to output
  gets() - reads string from input
  puts() - writes string to output
- File – fopen(), fclose(), fprintf(), fscanf(), fread() and fwrite()